| http://www.ece.umd.edu/~pabshire/enee312h.htm | due Thursday, April 11, 2002 |
| --- | --- |

- A particular bipolar IC process has the following tolerances in the dimensions and parameters of an npn transistor:

NDE = 1.2x1019 ± 1018 cm-3, WE = 500 ± 40 nm 
NAB = 4x1017 ± 2x1016 cm-3, WB = 350 ± 30 nm 
NDC = 4x1016 ± 1015 cm-3, WC = 1 ± 0.05 m

The emitter area is AE = 100 m2, and the collector area is AC = 750 m2.

  - Assuming that the parameter and dimensional variations are independent, find the average and variation of the saturation current IS.

  - For a fixed base-emitter bias VBE = 720 mV and base-collector bias

VBC = -2.3V, find the average and variation of the collector current IC.

  - Assuming that the parameter and dimensional variations are independent, find the average and variation of the forward current gain .

  - Find the minimum and maximum values of the forward current gain  for this process, by using the extreme values of the device parameters and dimensions.

- This exercise covers the qualitative effects of parameter and dimensional changes on the model parameters of an npn transistor.  In the following table, fill in each entry with +, -, or 0 to represent an increase, a decrease, or no effect as a result of an increase in the parameter in the left-hand column.  You may use the saturation current as defined in Sedra & Smith.  The operating point (IC, VCE) remains fixed.

| Parameter | Forward gain | Reverse gain | Saturation current IS | Early Voltage VA |
| --- | --- | --- | --- | --- |
| NDE |  |  |  |  |
| WE |  |  |  |  |
| DhE |  |  |  |  |
| NAB |  |  |  |  |
| WB |  |  |  |  |
| DeB |  |  |  |  |
| NDC |  |  |  |  |
| WC |  |  |  |  |
| DhC |  |  |  |  |

- –   7) Complete Sedra & Smith problems 4.63, 4.85, 4.96, 4.133, 4.135

Research Question:

What is a translinear circuit?  Who invented the name “translinear”?  Why?

How are translinear circuits related to bipolar junction transistors?

Provide the citation information for the first, definitive publication on translinear circuits.

Hint: The publication appeared in the journal Electronics Letters.