## Slide 1: Adjoint Methods in Charged Particle Dynamics or When the solution to your problem is not your problem. Thomas M. Antonsen Jr. Department of Electrical and Computer Engineering Department of Physics Institute for Research in Electronics and Applied Physics University of Maryland, College Park

## Slide 2: Example Jackson, Classical Electrodynamics Problems 1.12 and 1.13
A charge q is placed at an arbitrary point, xo, relative to two grounded, conducting electrodes.
What is the charge q1 on the surface of electrode 1?
Repeat for different x0
q
x0
q1
q2
B1
B2

## Slide 3: Solution – Green’s Reciprocation Theorem
Prob #1
Your Problem
BC:
Green’s
Theorem
Prob #2
Adjoint (Not your) Problem
BC:
When the dust settles:
0
0

## Slide 4: George Green 1793-1841
Physics Today Dec. 2003
Born in Nottingham (Home of Robin Hood)
Father was a baker
At age 8 enrolled in Robert Goodacre’s Academy
Left after 18 months (extent of formal education pre age 40)
Worked in bakery for 5 years
Sent by father to town mill to learn to be a miller

## Slide 5
Fell in love with Jane, the miller’s daughter.
Green’s father forbade marriage.
Had 7 children with Jane.
Self published work in 1828
With help, entered Cambridge 1833, graduated 1837.
Theory of Elasticity, refraction, evanescence
“Discovered” by Lord Kelvin in 1840.
Died of influenza, 1841
Green’s Mill: still functions

## Slide 6: Features of Problems Suited to an Adjoint Approach
Many computations need to be repeated.
(many different locations of charge, q)
Only a limited amount of information about the solution is required.
(only want to know charge on electrode #1)

## Slide 7: Relation to Reciprocity
Example:
- Antenna sending and receiving radiation patterns are equal due to time reversal symmetry of ME.
- Direct calculation of receiving pattern requires many simulations
- Instead, calculate sending pattern and invoke reciprocity
V
V
Receiving
Sending

## Slide 8: Other Examples of Reciprocity
Electrostatics Symmetry of the Capacitance Matrix
Electromagnetics Symmetry of the Inductance Matrix
Symmetry of Scattering Matrix
Collisional Transport: Onsager Symmetry of off-diagonal elements of transport matrices.
Temperature gradient  Electric current
Electric field  Heat flux
Neoclassical Tokamak Transport
Pressure gradient  Bootstrap Current
Toroidal E-field  Ware particle flux

## Slide 9: Adjoint Methods in Engineering

## Slide 10
Optimize shape
to minimize drag.
Result is also aesthetically appealing.
Super Computer
Courtesy, Elizabeth Paul

## Slide 11
1985 Volvo 240 DL
Oops, coding error.

## Slide 12: Adjoint Approach in Plasma and Beam Physics
Neoclassical Transport, F. Hinton, and R. Hazeltine, Rev. Mod Phys, 48 (2) , 1976
Calculation of beam driven currents in magnetized plasmas, S. Hirshman, PoF, 23, 1238 (1980).
Calculation of RF current drive in magnetic confinement plasma configurations, TMA and K. Chu PoF 25, (1982)
Calculation of RF induced transport in magnetic confinement plasmas, TMA and K. Yoshioka, PoF 29, (1986), Nucl. Fusion, 26 (1986).
Shot noise on gyrotron beams, TMA, W. Manheimer and A. Fliflet, PoP (2001).

## Slide 13: RF Current Drive in Fusion Plasmas
Magnetic Confinement: ITER
US-EU-Russia-Japan-India Collaboration
Will be built in Cardarache France
Completion 2016??
http://www.iter.org/
Poloidal magnetic field
Toroidal current
a person
Injecting RF waves can drive a toroidal current. N. Fisch PRL (1978)

## Slide 14: RF Current Drive Efficiency
Original Langevin Treatment: Nat Fisch, PRL (1978)
RF pushes particles in velocity space.
Collisions relax distribution back to equilibrium.
What is the current generated per unit power dissipated? J/PD
= RF induced velocity space particle flux
ψ inversely proportional to collision rate

## Slide 15: RF Current Drive Efficiency
RF pushes particles in velocity space.
Collisions relax distribution back to equilibrium.
N. Fisch: Current generated in parallel direction even if push is in perpendicular direction
electron velocity space

## Slide 16
For a Homogeneous Plasma, we want to solve steady state kinetic equation
Linearized collision operator
RF induced velocity space flux
Then find parallel current
Adjoint problem: Spitzer-Harm
Distribution function driven by a DC electric field.
Parallel current
Adjoint Approach: S. Hirshman, PoF, 23, 1238 (1980),
TMA and KR Chu, PoF 25, (1982)
Problem #1
Problem #2

## Slide 17: Toroidal Geometry Makes a Difference, TMA and KR Chu, PoF 25, (1982)
Outside
Inside
streaming
Magnetically trapped particles

## Slide 18: Recent Adjoint Approaches
Beam optics sensitivity function, TMA, D. Chernin, J. Petillo, Phys. Plasmas 26, 013109 (2019); doi: 10.1063/1.5079629
Stellarator Optimization and Sensitivity, E. Paul, M. Landreman, TMA, J. Plasma Phys. (2019), vol. 85, 905850207, J. Plasma Phys. (2021), vol. 87, 905870214
Optimization of Flat to Round Transformers in Particle Accelerators, L. Dovlatyan, B. Beaudoin, S. Bernal, I. Haber, D. Sutter and TMA, Phys Rev Accel and Beams V25, 044002 (2022).
Adjoint Equations for Beam-Wave Interaction and Optimization of TWT Design, A. Vlasov, TMA, D. Chernin and I. Chernyavskiy, IEEE Trans. Plasma Sci. V. March (2022).
Give a child a hammer and everything becomes a nail.

## Slide 19: Global Beam Sensitivity Function for Electron Guns
Goal
Derive and Calculate a function that gives the variation of specific beam parameters to
- variations in electrode potential/position
- variations in magnet current/position
Can be used to
- establish manufacturing tolerances
- optimize gun designs
Should be embedded in gun code (e.g. Michelle)

## Slide 20
Emitter
Focus
Electrode
Ground
1 cm
– HV
Matching
Section
Solid Model of Electrodes
Thermionic Cathode Electron Gun
Cut away view of trajectories
Emitter
Focus
Electrode
Anode
What shape to make electrodes?
Beam is compressed

## Slide 21
Code (Michelle) solves the following equations:
K
A
Equations of motion for N particles j=1,N
Accumulates a charge density
Solves Poisson Equation
Iterates until converged
Michelle: Petillo, J; Eppley, K; Panagos, D; et al., IEEE TPS 30, 1238-1264 (2002).
Start with vacuum fields

## Slide 22: Sensitivity Function
K
A
C
Basic question: How do small changes in position or potential of anode affect the properties of the beam leaving the gun?
Beam leaves here
Conventional approach: trial and error. Do many simulations with different anode potentials or positions select the best based on some metric measured at the exit.

## Slide 23: It will be shown …
K
A
C
K
A
C
Problem #1
Leads to change in RMS beam radius
Wall displacement changes potential on unperturbed surface.
Problem #2
Reverse and perturb electron coordinates
Calculate and record change in normal E.
Is the sensitivity function
Electrons run backwards
Sensitivity function

## Slide 24: Hamilton’s Equations H(p,q,t) Conserve Symplectic Area
perturbed orbit #1
perturbed orbit #2
Area conserved for any choice of 1 and 2

## Slide 25
Reference Solution + Two Linearized Solutions
Two Linearized Solutions
subject to different BC’s
Can show
true
adjoint
Reference Solution
Perturbation
Generalized Green Theorem

## Slide 26
Generalized Green’s Theorem
Problem #1 (true problem) Unperturbed trajectories at cathode, Perturbed potential on boundary.
Problem #2 (adjoint problem) Perturbed trajectories at exit, Unperturbed potential on boundary.
Sensitivity Function

## Slide 27: Vertical Displacement of the Beam
Vector plot of the ‘sensitivity’ or Green’s function
‘Direct’ MICHELLE Simulation with
Perturbed Anode Voltages
Predicted displacement / Calculated displacement = 0.9969

## Slide 28: Numerical Accuracy
Problem #2 (adjoint problem) Perturbed trajectories at exit, Unperturbed potential on boundary.
Problem #1 (true problem) Change anode voltage, find change in RMS radius.

## Slide 29: AO 2.4-4: John Petillo, Serguei Ovtchinnikov, Aaron Jensen (Leidos), Philipp Borchard (Dymenso) Kyle Kuhn, Heather Shannon, Brain Beaudoin TMA. (U. Maryland) Application: 2D parallel plate sheet beam
Forward Case: Grounded Inserts top and bottom
Direct Perturbation Case: Electrode inserts on top and bottom set to DV DV tested from 1 – 10,000 V
Neumann
Neumann
Forward Case
Direct Perturbed Case
Reverse-Beam Adjoint Method Case
DV=2000 V
Perturbed Dpx = l*pz0
V=0
DV=0
V=0
Electrode Inserts
Or Perturbed Dx = l*H

## Slide 30: Mean Displacement: 2D parallel plate sheet beam - Manufacturing sensitivity to beam centering offset
Results of direct vs. adjoint methods agree to within 0.20%.
Verification: Hamiltonian Approach Excellent first successful Adjoint method to beam transport in a magnetic field.
Results:
  As the perturbed-case voltage values became small enough it easily entered the linear regime.
  There is very a broad range of both L and DV where the results are all in a linear regime.
Adjoint method predicted the deflection sensitivity to within 0.2%

## Slide 31: AO 2.4-2 – Optimization of TWT Design by Using Adjoint Approach A. Vlasov, T. M. Antonsen Jr., D. Chernin, I. Chernyavskiy
,
Maximize:
Minimize:
Maximize:
Distance between gaps (two sections).
3 different goal functions
2 optimization parameters
Optimization of Small Signal Gain

## Slide 32: 3D MHD Equilibria
Wendelstein 7-X
Max Planck Institute for Plasma Physics (IPP)
Greifswald, Germany Completed 2015
Coils
Vacuum Vessel
Plasma

## Slide 33: Optimization of Stellarator Equilibria
Figures of Merit (FoM) - Examples
Plasma Beta, Rotational Transform, Quasi-symmetry
FoMs depend on boundary or coil shapes
Shape Gradient Sensitivity Functions
gradient based optimization
establish tolerances
C. Othmer, J. Math. Industry 4, 6 (2014). DRAG
Landreman and Paul, 2018 Nucl. Fusion 58 076023,
E. Paul, M. Landreman, TMA, J. Plasma Phys. (2019), vol. 85, 905850207,
J. Plasma Phys. (2021), vol. 87, 905870214
Rotational transform

## Slide 34: Adjoint Symmetry Simplifies Calculations
Adjoint Approach to gradient calculation
> 500 X Speed – Up over direct calculation
Uses VMEC & DIAGNO
Hirshman and Whitman, 1983 Phys. Fluids 25 3553
H.J. Gardner 1990 Nucl. Fusion 30 1417
Different Figures of Merit Possible
Plasma pressure – beta
Rotational transform
Toroidal current
Neoclassical radial transport -1/ν regime
Energetic particle drifts
Quasi-symmetry
Others
Surface shape sensitivity
Coil location sensitivity

## Slide 35: 3D MHD Toroidal Equilibrium
Assume good flux surfaces in plasma
Poloidal flux
Toroidal Flux
In vacuum
coil current
Rotational transform
Coils
In plasma

## Slide 36: Linear Perturbations to Equilibrium
Generalized Forces:
Changes in current/shape/location of coils
Added pressure tensor
Change in poloidal flux profile
Generalized responses:
Changes in vacuum fields
Changes in magnetic field
Changes in toroidal current profile

## Slide 37: Generalized Forces and Responses
Forces:
Coil currents
Pressure tensor
Rotational transform
Responses
Vacuum fields
Plasma displacement
Toroidal current profile
More generically,
for two different perturbations
Onsager Symmetry Gives

## Slide 38: Onsager Symmetry for 3D MHD Equilibria Self-adjoint MHD Force Operator
Pressure - Displacement
Rotational transform –Toroidal current
Surface displacement
True
Adjoint

## Slide 39: Specify BC’s & Constraints
Pressure - Displacement
Rotational transform –Toroidal current
Surface displacement
True
Adjoint
Make this appear to be change in FoM
Sensitivity function

## Slide 40: Specify BC’s & Constraints
Pressure - Displacement
Surface displacement
True
Adjoint
Make this appear to be change in FoM
Sensitivity function

## Slide 42: Optimization of Focusing Magnets in Accelerator Lattices
The University of Maryland Electron Ring
UMER is a fully functional electron storage ring

## Slide 43: UMER Systems and Layout
167 Magnets, power supplies &
controls.
x
x
x’=dx/ds
x’=dx/ds
Transverse Phase space
Want to avoid trajectories outside here

## Slide 44: Focusing Basics
Quadrupole Magnetic Field
Focusing in x-direction
Defocusing in y-direction
qv – out of page
32 Quadrupole
magnets
Field strength increases linearly with distance from the axis

## Slide 45: FODO Lattice
Alternate focusing and defocusing orientations
Qualitative explanation: beam passes through focusing quad when it is big (strong fields). Passes through defocusing quad when it is small (weak fields). Net effect is focusing.
32 Quadrupole
magnets
Beam distribution depends on many parameters How to optimize?

## Slide 46
Flat Beam
Round Beam
Flat to Round and Round to Flat transformers are proposed for cooling of hadron beams. Ya. Derbenev, Adapting optics for high-energy electron cooling, Tech. Rep. UM-HE-98-04-A (1998).
Cylindrical hadron beam cools via collisions when co-propagated with electron beam.
Optimization of Flat to Round Transformers Using Adjoint Techniques*
L. Dovlatyan, B. Beaudoin, S. Bernal, I. Haber, D. Sutter and T. M. Antonsen Jr , Phys Rev Accel and Beams V25, 044002 (2022).

## Slide 47: Steps
1. Derive system of moment equations (include self fields)
2. Linearize (to compute parameter gradient)
3. Find adjoint system
4. Decide on Figures of Merit
5. Optimize by Gradient Descent
Flat Beam
Round Beam

## Slide 48: Moment Equations
Symbols –PIC
Lines – Moment Eqs.
Depend on magnet parameters

## Slide 49: More Optimization
Continuous magnetic field profiles
Variable magnet orientations

## Slide 50: Circular Accelerators-Periodicity
Particles return to initial plane.
Need to maintain periodicity of distribution, not individual orbits
Big problems:
Do periodic distributions exist? Most likely no.
How to relaunch particles to optimize?
Start here with 4D particle coordinates
Particles + Periodicity = Problems
Solve Eqs. of motion and self fields

## Slide 51: Conclusion
Adjoint methods are a powerful way to evaluate parameter dependences in many systems involving charged particle dynamics.
Thank you.

## Slide 52: Moment Equations
Transverse phase space:
The second order moments are averages of the 4 by 4 elements of the Sigma matrix.
Moments: Q, P, E, L
Angular momentum

## Slide 53: Linearized System
Base case
Linear perturbation due to true change in parameters
Adjoint system
Change in magnet parameters
Sensitivity functions

## Slide 54: Figure of Merit and Gradient
Constant radius, Round
Radial force balance, Rigid rotation

## Slide 55: Optimization – Space Charge Compensation

## Slide 56: Next Step – Circular Accelerators
Z=Zi
Z=Zf
Beam Particles
Solve Moment Eqs.
Periodicity: Enforce
Figure of Merit F(X,a)
Optimize: Minimize
a = parameter list
Constrained Optimization by Multiple Relaxation
Adjoint with a Chaser !

## Slide 57: Next Step – Circular Accelerators
Z=Zi
Z=Zf
Beam Particles
Solve Moment Eqs.
Periodicity: Minimize
Figure of Merit F(X,a)
Minimize
This is the tricky term

## Slide 58: The Tricky Term
This is the tricky term
Requires evaluating and inverting large matrices

## Slide 59: Constrained Optimization by Multiple Relaxation
Adjoint with a Chaser !
or
The equilibrium
The chaser
Parameter evolution
Only first derivatives required (6)

## Slide 60: How is it Supposed to Work
X tends to local equilibrium
The chaser tends to a slightly different equilibrium
So that “a” evolves “slowly”.
Allow a to change:
The X equilibrium changes

## Slide 61: Constrained Optimization by Multiple Relaxation
Adjoint with a Chaser !
or
The equilibrium
The chaser
Parameter evolution
Only first derivatives required (4)

## Slide 62: Moment Eqs. – Circular Accelerators
Z=Zi
Z=Zf
Beam Particles
Solve Moment Eqs.
Periodicity: Minimize
Solve Adjoint Eqs.
Figure of Merit F(X,a)
Can be evaluated with 6 solutions of adjoint Eqs.

## Slide 63: Conclusion
Adjoint method allows for optimization of Round to Flat and Flat to Round transformers.
Periodic lattices may (?) be handled by “Adjoint with a Chaser”. We are currently testing using moment equations
Formalism extended to treat particle description - done
“Adjoint with a Chaser” may be extended to Stellarator optimization, with a side of ALPO©️.

## Slide 64: Conclusion: Next Steps
Change in magnetization current
sensitivity function
Add Magnetic field
Add time dependence
Implement in an optimization routine

## Slide 65: Basic Formulation – Linear Algebra
We wish to solve :
And then evaluate for each B:
Instead solve for y once:
Then:
for many B’s.
D(B) is the answer.

## Slide 66
Radial Flux driven by RF

## Slide 67
RF Induced Transport
Perturbed neoclassical DF
TMA and K. Yoshioka, PoF 29, (1986)
Response to a radial gradient
Fluctuation induced radial flux

## Slide 68: Jacobian Matrix – M(t)
2N Eiegenvectors and Eigenvalues of M
2Nx2N
Solutions come in N pairs-
Eigenvectors from different pairs orthogonal

## Slide 69
Beamstick: Gun Baseline Geometry Particle Trajectories at Actual Voltages
Vk = -25.1 kV
Vma = -20.2 kV
Ik = 39.8 mA
It = 16.7 mA
Transmission = 42%
10X
Approved for public release; Distribution unlimited

## Slide 70: Theoretical Study of Statistical Variations Example of the Adjoint Method in Action
= Beam centroid displacement at gun exit
 = Small change or error in anode or other electrode potential
= Sensitivity (Green’s) function
Problem: Compute the displacement of the beam in a sheet beam gun due to a small change in anode potential or a small displacement of the anode:
MICHELLE Simulations of Sheet Beam Gun
‘Perturbed’ case:
Beam centroid at gun exit is displaced
‘Perfect’ case:
Beam centroid at gun exit is on axis
The adjoint method gives us a way to compute the displacement of the beam without re-running MICHELLE:

## Slide 71
Code (Michelle) solves the following equations:
K
A
Hamilton’s Equations for N particles j=1,N
Accumulates a charge density
Solves Poisson Equation
Iterates until converged

## Slide 72
RMS radius sensitivity
Cathode E-normal has the largest “sensitivity”
Anode E-normal sensitivity
Anode normal AK-Gap values

## Slide 73: Adjoint Equations
Base case
Linear perturbation due to change in parameters
Adjoint system
Can show
Arbitrary Changes in focusing magnets
Adjoint sensitivity

## Slide 74: Change in Figure of Merit
Can show
Arbitrary Changes in focusing magnets
Adjoint sensitivity
Figure of Merit

## Slide 75: Focusing Basics
Quadrupole Magnetic Field
Focusing in x-direction
Defocusing in y-direction
qv – out of page
32 Quadrupole
magnets
Field strength increases linearly with distance from the axis

## Slide 76: FODO Lattice
Alternate focusing and defocusing orientations
Qualitative explanation: beam passes through focusing quad when it is big (strong fields). Passes through defocusing quad when it is small (weak fields). Net effect is focusing.
32 Quadrupole
magnets
Beam distribution depends on many parameters How to optimize?

## Slide 77: Circular Accelerators-Periodicity
Need to maintain periodicity of distribution, not individual orbits
Pick adjoint coordinate perturbations to realize desired FoM
z=0, z=L
Sensitivity to changes in magnet parameters
Too hard!

## Slide 78: Effective Area – Antenna Gain
V
V
Receiving
Sending
Power per unit solid angle
Power received
Effective area
Incident intensity
gain
I