## Slide 1: Vacuum Electronics Theory, Modeling & Simulation Thomas M. Antonsen Jr. Institute for Research in Electronics and Applied Physics Departments of ECE and Physics University of Maryland March 3, 2022

## Slide 2: Acknowledgements
People
NRL
Simon Cooke
Alexander Vlasov
Igor Chernyavskiy
Baruch Levush
LEIDOS
David Chernin
John Petillo
Agencies
NRL
ONR
DoE
AFOSR
AFRL

## Slide 3: Outline
Part I
Role of Simulation
Classification of code types
Part II
Geometry Based Codes, FDTD-PIC
Part III
Reduced Description Design Codes

## Slide 4: Why is Modeling and Simulation Important?
• Understanding of basic physical processes
• Understanding and diagnosing particular experiments
• Designing improved experiments
• Optimizing designs for “ first pass success”

## Slide 5: AREAS of PROGRESS
Improved Physics Models
Find better (compact) descriptions of what’s going on inside a VE device.
More Efficient Algorithms
Solve the governing equations with fewer operations and/or less memory usage.
New Computing Architectures
Restructure your code to take advantage of new hardware.

## Slide 6: Apology: I am not really a computer expert.
Computation

## Slide 7: Classification of Vacuum Electronics Design Codes
Geometry Based Codes
Commercial CEM - to characterize EM properties of structure
Full PIC - first principles description, but time consuming
3D Beam Optics - gun and depressed collector
Thermal/Mechanical - heat and stress
Reduced Description Codes
1D- 2.5D Parametric - simple beam model, scope parameters, study trade-offs
2.5D Hybrid PIC - fields in beam tunnel represented more accurately, expectation of quantitative accuracy

## Slide 8: 3D Geometry Based Codes
  Electrostatic Fields & Particles (Gun codes)
    MICHELLE (Leidos)
    Beam Optics Analyzer (CCR)
    Electron Optics Simulator (UESTC)
    Opera (Cobham)
  Magnetostatics
    Maxwell (ANSYS)
  Electromagetic Fields (Frequency domain)
    HFSS (ANSYS)
    Analyst (NI / AWR)
    HFCS (UESTC)
  Electromagnetic Fields & Particles (Time domain)
    VSim (Tech-X)
    CST Microwave/Particle Studio (CST)
    ICEPIC (AFRL)
    Neptune (NRL)
    MAGIC (Orbital ATK)
    KARAT

## Slide 9: Classification of Vacuum Electronics Design Codes
Geometry Based Codes
Commercial CEM - to characterize EM properties of structure
Full PIC - first principles description, but time consuming
3D Beam Optics - gun and depressed collector
Thermal/Mechanical - heat and stress
Reduced Description Codes
1D- 2.5D Parametric - simple beam model, scope parameters, study trade-offs
2.5D Hybrid PIC - fields in beam tunnel represented more accurately, expectation of quantitative accuracy

## Slide 10: Computational Electromagnetics Codes (CEM)
Frequency Domain: Assumes time harmonic fields
Typically unstructured mesh
Driven solutions
Scattering matrices
Antennas
Eigenmode solution
Normal modes of structures
Dispersion curves periodic structures
Time Domain: Fields evolve in time
Typically structured mesh
Finite difference time domain (FDTD)
Frequency domain data extracted by Fourier Transform

## Slide 11: Mesh Types (S. Cooke)
  Pros:
Structured mesh elements generally smoothly evolve from one to another
    Higher accuracy  lower numerical noise
Logical ordering of data makes…
    Particle tracking easier/faster
    Data more compact – allowing larger meshes
  Cons:
Meshing is usually a manual process, and can be time consuming
Some geometries can be intractable to mesh
  Cons:
Unstructured mesh elements have no distinct pattern or smooth connectivity
    Higher numerical noise  lower accuracy
Non-Logical ordering of data makes… Particle tracking more complex
Data is accessed through linked lists, and not as compact or computationally efficient
  Pros:
Meshing is a much more automated process, with less manual interaction. Trade user time for computer time.
Can mesh just about any geometry
Structured: logical ordering
0
0
1
1
2
2
(1,0)
(1,1)
(1,2)
(2,0)
(2,1)
(2,2)
(0,0)
(0,1)
(0,2)
Unstructured: no specific ordering
(0)
(6)
(7)
(1)
(8)
(2)
(3)
(5)
(4)
(10)
(9)

## Slide 12: Finite Difference Time Domain (FDTD)
  The Cartesian “Yee” Grid
Store electric fields on the edges of the grid cells
Store magnetic fields on the faces of the grid cells
Express Maxwell’s Equations in discrete form

## Slide 13: Eliminating stepped boundaries in structured meshes
  Traditional “Stair-step” algorithm
    Each cell is either metal or vacuum
    Leads to poor simulation accuracy
  Dey-Mittra “Cut-cell” algorithm
    Use fractions of edge lengths and face areas that lie in the vacuum to correct the geometry
vacuum
vacuum
metal
metal
grid

## Slide 14
14
(2) Compute effective permittivity for each cut cell edge
(3) Compute symmetric matrix elements to couple adjacent edges
(1) Identify edges cut by the interface
(4) Resulting matrix is symmetric with sparse off-diagonal components
ε1
ε2
ε1
ε1
ε1
ε2
ε2
ε2
Discrete Cut-Cell Dielectric Model, S.Cooke
ε1
ε2

## Slide 15: Convergence wrt grid size (Cooke) Eigenmode calculation
Stair-step approximation
Sub-cell averaging
0.1%
0.1%
O(h2)
Error
Error
# of cells
# of cells

## Slide 16: CEM calculation of FW Fields
2p
Symbols CEM
Lines - model

## Slide 17: Impedance and Scattering Matrices
Zij
Input
Output
IG1
29 x 29
IG2
IGn
Output
Gaps
Ports
Folded waveguide

## Slide 18: Classification of Vacuum Electronics Design Codes
Geometry Based Codes
Commercial CEM - to characterize EM properties of structure
Full PIC - first principles description, but time consuming
3D Beam Optics - gun and depressed collector
Thermal/Mechanical - heat and stress
Reduced Description Codes
1D- 2.5D Parametric - simple beam model, scope parameters, study trade-offs
2.5D Hybrid PIC - fields in beam tunnel represented more accurately, expectation of quantitative accuracy

## Slide 19: First Principles Basic Physics Model

## Slide 20: Particle in Cell (PIC) Algorithm

## Slide 21: Interpolation Gather – Scatter #1 Gather
Ex
Ex
Ey
Ey
Fields are interpolated from edges of a cube to location of a particle in the cube.

## Slide 22: Interpolation Gather Scatter: #2 Scatter
Each Component of J needs to be calculated on the edge associated with the corresponding component of E.
J needs to be evaluated at the half time step. The velocity is known at the half time step, position is known at the time step.
Ex
Ex
Ey
Ey
v

## Slide 23: Challenges in PIC Simulations of Vacuum Electronic Devices

## Slide 24: GPU Accelerated PIC Simulations
NEPTUNE
NRL Code Neptune was created to target GPU simulation
Based on existing algorithms – adapted for the GPU architecture
  FDTD algorithm for electromagnetics (explicit time step)
Conformal representation of metal surfaces (accurate geometry discretization)
  Boris algorithm for particle time step, with charge-conserving current deposition
Simulation speed (normalized to 6-core “Sandy Bridge” CPU)
GPU
GPU
CPU
CPU
13.7M cells, 1M particles

## Slide 25: Electromagnetic PIC Simulation (S. Cooke)
Direct discretization of interaction physics based on detailed 3D device geometry
    Finite-Difference Time-Domain (FDTD) model for electromagnetic fields
    Full-spectrum of RF field
    Detailed beam model using a large collection of macro-particles to capture the spatial and energy/momentum distribution
    Fully self-consistent beam-wave interaction
Benefits for device design:
    Accurate device performance prediction for both existing and novel designs
    Predicts stability to oscillations
    Full EM solver: , couplers, windows
Limitations:
    Low throughput – many hours/simulation
    Requires a complete geometry description
Single-stage Helix TWT amplifier
Time
Electron Energy
(Neptune 3D EM-PIC simulation)
minutes

## Slide 26: Neptune Simulations of NRL G-Band SW TWT
NRL 220 GHz Serpentine TWT amplifier (simulations performed using measured dimensions)
Data 11.7kV
Neptune 11.7kV
Small Signal Gain
Transfer curves
11.7kV
11.9kV
K. T. Nguyen et al., “Design Methodology and Experimental Verification of Serpentine/Folded-Waveguide TWTs” IEEE T-ED Special Issue on Vacuum Electronics, 2014
Good Agreement between Neptune predictions and measurements

## Slide 27: Classification of Vacuum Electronics Design Codes
Geometry Based Codes
Commercial CEM - to characterize EM properties of structure and static magnetic fields
Full PIC - first principles (but structure deficient)*
3D Beam Optics - gun and depressed collector
Thermal/Mechanical - heat and stress
Reduced Description Codes
1D- 2.5D Parametric - to scope parameters, sensitivity
2.5D Hybrid PIC - fields in beam tunnel represented in modes
Many codes used, codes talk to each other, some codes are duplicative

## Slide 28: CHRISTINE: a Multifrequency Parametric Simulation Code for Traveling Wave Tube Amplifiers TMA and Baruch Levush NRL/FR/6840-97-9845 (1997) IEEE TRANSACTIONS ON PLASMA SCIENCE, VOL. 26, NO. 3, JUNE 1998
found
in separate calculation
Particles: Energy and time of flight vs z
Space charge, disks
Helix
Structure Impedance
Also: Internal Sheath Helix Model
Structure wave number

## Slide 29: Time Domain Simulation Standard PIC
t
t+dt
time
0
L
z
System state specified
Signal and
particles injected
Trajectories
Fields advanced in time domain
Positions interpolated to a grid in z
Carrier and its harmonics must be resolved

## Slide 30: Frequency & Slow - Time Domain Hybrid Simulation
Signal
Period T=2p/w
Trajectories
z
time
0
L
z+dz
4. Slow time or iterative update
If counter propagating waves present, iterative convergence
3. Forward propagating waves integrated with particles
2. Group of particles entering in one period are advanced together
1. Fields are assumed to be time periodic.

## Slide 31: Sheath Helix Model TMA and Baruch Levush NRL/FR/6840-97-9845 (1997) IEEE TRANSACTIONS ON PLASMA SCIENCE, VOL. 26, NO. 3, JUNE 1998
Helical tape is modeled as a cylinder with anisotropic conductivity.
Perfect conductor along helical path.
Perfect insulator transverse to path.
Wall
Sheath helix
Beam
Structure mode
Space Charge
Correction
Current density profile

## Slide 32: Basic Calculations
Phase
Space

## Slide 33: Multi Frequency – “Steady State”
ti(z)
z
Periodic time dependent signal
Each frequency component evolves in z
Integrations completed in one pass
Particles launched with entrance times covering one period

## Slide 34: Multi-Frequency Simulations
Intermodulation
Traveling-Wave Tube Devices with Nonlinear Dielectric Elements,
Thomas M. Antonsen, Jr., and Baruch Levush,
IEEE TRANSACTIONS ON PLASMA SCIENCE, VOL. 26, NO. 3, JUNE 1998
16 QAM digital signal
From Frequency-Domain Physics-Based Simulation to Time-Domain Modeling of Traveling-Wave Tube Amplifiers for High Data-Rate Communication Applications
Pedro N. Safier, Vasily Dronov, Thomas M. Antonsen, Jr., Joe X. Qiu, Bruce G. Danly, and Baruch Levush,
IEEE TRANSACTIONS ON MICROWAVE THEORY AND TECHNIQUES, VOL. 54, NO. 10, OCTOBER 2006

## Slide 35: Beam Models and Self fields
Representation of a bunched beam
z
Christine 1D
Christine 3D (2 ½ D)
A Three-Dimensional Multifrequency Large Signal Model for Helix Traveling Wave Tubes, David Chernin, Thomas M. Antonsen, Jr., Baruch Levush, and David R. Whaley IEEE TRANSACTIONS ON ELECTRON DEVICES, VOL. 48, NO. 1, JANUARY 2001
Charge disks
Charge rings

## Slide 36: Self Fields - Comparison with Experiment
Charge and current density deposited on a grid in r at each z.
Longitudinal self fields
Transverse self fields
Intercepted current
Experimental and simulated drive curves of C-Band DVT TWT: (a) logarithmic drive curve, (b) linear drive curve, and (c) intercept current variation with
input drive power. Beam voltage = 4.8 kV, current = 146 mA, operating frequency = 4.75 GHz.
More elaborate models

## Slide 37: An Improved Representation of AC Space-Charge Fields in Steady-State Simulation Codes for Linear-Beam Tubes D. Dialetis, D. Chernin, T. M. Antonsen, Jr., and B. Levush IEEE TRANSACTIONS ON ELECTRON DEVICES, VOL. 54, NO. 4, APRIL 2007
Wall
Helix
Dielectric
Beam
In CEM code insert current
In interaction code
Structure mode
Space Charge
Correction

## Slide 38: Devices with Gaps – Christine and TESLA
38
Folded Waveguide
CL
Coupled Cavity
Beam
General Approach
Separate domains
Beam tunnel
Structure
A.P.Kuznetsov et al. UDC621.385.6
Radiophysics and Quantum Electronics, Vol. 47, Nos. 5–6, 2004
Klystrons

## Slide 39: Parametric Treatment of Structures with Gaps
Particles: Energy and time of flight
Coupled Cavity, Folded WG
Space charge

## Slide 40: Parametric Approach: CHRISTINE-FW
Circuit model:
  Dispersion and impedance:
“Transmission Line Model for Folded Waveguide Circuits”, T.M. Antonsen, Jr., et al., IEEE Trans. on Electron Devices, 60 (9), 2013.
Comparison of model dispersion and impedance with CEM calculations

## Slide 41: Hybrid Model - TESLA
41
Dispersion and Impedance fit to circuit model
Structure fields pre- calculated, fit to circuit model, couple through gaps
Full solution of beam tunnel fields and electron motion.
CL
Gun
RF Input
RF Output
Collector
Steps
Compute dispersion and impedance using CEM.
Fit to circuit model: Curnow , FW or other
3. Import to TESLA
TESLA
Goal: eliminate circuit model

## Slide 42: Separation of domains in large-signal model:
Beam-tunnel
simulation boundary
separation of domains:
introduce simulation boundary dividing the whole device into two domains:
  (1) beam-tunnel and (2) external circuit
use distinct representation of the fields in each domain
couple the two domains on the boundary between them
External circuit
Beam tunnel fields: Sum over local cross-section eigenmodes provides full solution of Maxwell’s Equations
local cross-section eigenmodes
sum over temporal harmonics
The field representation used inside the beam-tunnel is complete in describing beam-wave interaction. Keep this approach in our future model!
Domain 1: beam-tunnel
e--beam
Geometry-driven
large-signal modeling
Domain 2: external slow-wave structure
Physical fields represented by Electromagnetic Modes of an arbitrary slow-wave structure

## Slide 43: Impedance and Scattering Matrices
Zij
Input
Output
IG1
29 x 29
IG2
IGn
Output
Gaps
Ports
Folded waveguide

## Slide 44: Stitching Together Structure and Beam Tunnel Fields Z-Matrix
In a CEM code or circuit model,
place annular current source in each gap. One by one, compute voltage on each gap in response to each source
Also include input and output ports
Gaps
Ports
Step 1
Can be done with CEM code or circuit model

## Slide 45: Run Two Concurrent Beam Tunnel Simulations
Iteration
Impose tangential electric field based on current values of gap voltages VG
Solve beam tunnel twice: with (1) and without (2) beam
Compute effective gap currents
Repeat until converged.

## Slide 46: Impedance Matrix Characterization
Zij
Input
Output
IG1
29 x 29
IG2
IGn
Output
Gaps
Ports
Folded waveguide
B.Levush et. al. “A 1.8 kW Broad Band Ka-band TWT Power Booster”,
IVEC 2014.
Implemented Christine

## Slide 47: New Directions
Numerical Determination of Vacuum Electronic Device Stability, Chernyavskiy et al., IEEE TRANSACTIONS ON PLASMA SCIENCE, VOL. 48, NO. 12, DECEMBER 2020.
Structure Optimization, Adjoint Equations for Beam-Wave Interaction and Optimization of TWT Design, Vlasov et al., to be published, IEEE Trans. Plasma Sci.
Calculation and Application of Impedance Matrices for Vacuum Electronic Devices, Jabotinski et al., IEEE TRANSACTIONS ON ELECTRON DEVICES, VOL. 66, NO. 5, MAY 2019

## Slide 48
Thank You
Questions ?

## Slide 49: History (continued)
• Gyro devices
• Mode competition

## Slide 50: History (cont.)
• Free electron lasers

## Slide 51: 3D – Geometry Based Codes (S. Cooke)
  Magnetostatics
  Static magnetic fields for a given set of coils or permanent magnets
  Electromagetic Fields (Frequency domain)
  Eigenmodes of structures
  Structure Port Scattering Matrices
  Electrostatic Fields & Particles (Gun codes)
  Steady state charge flow guns, transport channels, depressed collectors
  Electromagnetic Fields & Particles (Time domain)
  Time dependent charged particle motion and field evolution

## Slide 52
MAryland
GYrotron
Code
Maggie
Improved by M. Botton and A. Vlasov

## Slide 53
CHRISTINE: a Multifrequency Parametric Simulation
Code for Traveling Wave Tube Amplifiers
Naval Research Laboratory
Washington DC
spectrum
Phase
space
Christine
Further developed by Dave Chernin 3D, CCTWT, FW

## Slide 54: A sweet of codes

## Slide 55: Codes Mature
MAGY  TESLA
I. Chernyavskiy, A. Vlasov
Christine
Helix  CCTWT,
FW, Klystron
D. Chernin