File: G:\coursesF20\610\610F20Hmwrk3.doc   RWN   09/15/20

ENEE 610 F20	Homework #3 Due Tu 09/29/20

!. For the following degree one circuit:

a. Find the Y, Z and S matrices for the 2-port.

b. From the resulting equations give the transfer function Vout(s)/Is(s)

c. Set up state equations using the current source Is as the input and voltage Vout as the output.

d. Use the state equations to check the result of part b.

2. Stae equations for modified Van der Pol equations are, with eps and r as parameters

dx/dt = y

dy/dt = -eps(x2+y2-r2)y – ω02x

a) Give the 2nd order ODE in x.

b) Set this up in Spice or Simulink and show that there is a limit cycle for r=1 and for each of three values of eps1=0.0001, eps2=1, eps3=10. In each case choose two different initial conditions:

x(0)=1/2, y(0)=1/2 and x(0)=5=y(0).

3. Assume that (nonlinear) multipliers are available, draw a circuit using capacitors, OTAs, and multipliers.