File: f:/coursesS10/303/303S10Midtrm.doc     RWN       03/25/10

ENEE 303 Midterm Exam, Spring 2010

100 points, 75 minutes, open book open notes. If stuck go onto the next problem. Good luck!

- (50 points, 30 min) For this circuit the forward beta is (f=200 and the reverse beta is (r=10; the Early voltage (forward and reverse) is infinite. Assume the base-emitter is biased at VBE=0.7V

  - (20 points) Find the Q point values of IB, IC and VCE.

  - (10 points) If by mistake the transistor is reversed, that is C and E are mistakenly interchanged, find the resulting Q point values of IB, IC and VCE.

  - (20 points) Compare the gmf and gmr, the gm values for the two cases, and give the resulting small signal voltage gain (input at b and output at c)  assuming RE is bypassed and ignoring Ra & Rb for signal (also ignore transistor capacitance) .

- (50 points, 30 min)

The following is a bi-directional current mirror. Assume that the NMOS are 4007 transistors (of  parameters:KP=20.54u, W=144u, L=8u, VTO=1.3, LAMBDA=15m)

and that the PMOS are completely complementary (that is of parameters :KP=20.54u, W=144u, L=8u, VTO=-1.3, LAMBDA=15m). Ignore transistor capacitors.

- (10 points) For zero port currents explain why the port voltages are zero and give values to all the drain currents.

- (10 points) Find the bias power consumed by the bi-directional current mirror (that is, when the port currents are zero).

- (20 points) Find the 2-port admittance matrix for small signal port variables (positive currents going into the port leads and voltages positive at the leads with respect to ground).

- (10 points) Place a 20 nanoFarad load capacitor, CL, across port 2 and give the resulting voltage gain v2(s)/v1(s) and give its poles and zeros..