| http://www.ece.umd.edu/~pabshire/enee312h.htm | due Tuesday, March 19, 2002 |
| --- | --- |

- The npn silicon transistor shown below is characterized by the following parameters: NDE = 5x1017 cm-3, = 3 m, = 0.1s, = 250 cm2/Vs 
NAB = 5x1016 cm-3, = 0.8 m, = 0.1s, = 1000 cm2/Vs 
NDC = 5x1015 cm-3, = 6 m, = 0.1s, = 500 cm2/Vs 
Start by checking whether the lengths  are small compared to the diffusion lengths, and use these results to compute the effective lengths .  The active cross-sectional area of the transistor is 5x104 cm2.  Use VT = kT/q = 0.025V and =1010 cm-3.

  - The transistor is operated in the forward active mode with VBE>0 and VBC=0.  Obtain numerical values for the base and emitter defects,  and.

  - The transistor is operated in the reverse active mode with VBC>0 and VBE=0.  Obtain numerical values for the base and collector defects,  and.

  - Obtain numerical values for  and.

  - Obtain numerical values for the parameters of the Ebers-Moll  model: IES, ICS,  and.

  - Show that.

- Two high-gain bipolar transistors have identical dimensions and identical emitter, base, and collector doping profiles, except that transistor A is npn and transistor B is pnp.  Indicate which device, if either, has the properties stated below and explain why.

  - Largest forward current gain

  - Smallest transconductance  with |IC| = 1mA

  - Largest base-collector diode saturation current ICS

  - Lowest parasitic base resistance

- Consider using the emitter-base junction of an npn transistor as a diode.  We want to compare the three possible connections illustrated below.

  - Find a relationship for the diode current ID as a function of VAB in terms of the Ebers-Moll parameters IES, ICS,  and of the transistor.

  - For which of these “diodes” is the saturation current “IS” the smallest? The largest?

  - For each of these connections find expressions in terms of the Ebers-Moll parameters for the ratio of the collector current to the emitter current.

  - Indicate on sketches of each of the connections the main current path through the device from A to B.

- –   7) Complete Sedra & Smith problems 4.3, 4.5, 4.10, 4.97

Research Question:

What is the Early effect?  Perform a literature search to find the original paper (nearly 50 years old!) in which Jim Early provides a quantitative explanation and model for the phenomenon.  Read the paper and comment on his explanation.