## Slide 1: ENEE244-02xx Digital Logic Design
Lecture 4

## Slide 2: Announcements
HW 1 due today.
HW 2 up on course webpage, due on Thursday, Sept. 18.
“Small quiz” in recitation on Monday, Sept. 15 on material from Lectures 1,2

## Slide 3: Agenda
Last time:
  Error Detecting and Correcting Codes (2.11, 2.12)
  Boolean Algebra (3.1)
This time:
  Boolean Algebra axioms and theorems (3.1, 3.2)
  Boolean Formulas and Functions (3.4)
  Canonical Formulas (3.5)

## Slide 4: Boolean Algebra

## Slide 5: Definition of a Boolean Algebra
A mathematical system consisting of:
  A set of elements [0/1 or T/F]
  Two binary operators (+) and () [OR/AND]
  = for equivalence, () indicating order of operations
  Where the following axioms/postulates hold:
  P1. Closure
  For all
  P2. Identity
  There exist identity elements in , denoted 0,1 relative to (+) and (), respectively.
  For all

## Slide 6: Definition of Boolean Algebra
  P3. Commutativity
  The operations (+), () are commutative
  For all
  P4. Distributivity
  ***Each operation (+), () is distributive over the other.
  For all :
  []
  []

## Slide 7: Definition of Boolean Algebra
  P5. Complement
  For every element there exists an element called the complement of such that:
  P6. Non-triviality
  There exist at least two elements such that

## Slide 8: Principle of Duality
(Except for P6), each postulate consists of two expressions s.t. one expression is transformed into the other by interchanging the operations (+) and () as well as the identity elements 0 and 1.
Such expressions are known as duals of each other.
If some equivalence is proved, then its dual is also immediately true.
E.g. If we prove: , then we have by duality:

## Slide 9: Theorems of Boolean Algebra
Theorem 3.2: Null elments:
For each element in a Boolean algebra:
.
Proof:
[by P2]
[by P5]
[by P4]
[by P2]
Second part follows from principle of duality.

## Slide 10: Theorems of Boolean Algebra
Theorem 3.4: The Idempotent law
For each element in a Boolean algebra:
Proof:
[by P2]
[by P5]
[by P4]
[by P5]
[by P2]
Second part follows from principle of duality.

## Slide 11: Theorems of Boolean Algebra
Theorem 3.5: The Involution Law
For every in a Boolean algebra,
Proof. We will use the fact that the complement is unique (Theorem 3.1 in textbook).
[by P5]
[by P3]
by uniqueness.
Moreover,
[by P5]
[by P3]
by uniqueness.

## Slide 12: Theorems of Boolean Algebra
Theorem 3.6: The absorption law
For each pair of elements in a Boolean algebra:
Proof:
[by P2]
[by P4]
[by Theorem 3.2]
[by P2]
Second part follows from principle of duality.

## Slide 13: Theorems of Boolean Algebra
Theorem 3.7: DeMorgan’s Law
For each pair of elements in a Boolean algebra:
Proof:
[by P4]
[by P3]
[by P5]
[by Theorem 3.2]
[by P2]
Analogous for multiplicative case.
Second part follows from principle of duality.
Note: Using Associativity of each operation (+), ().
Theorem 3.8

## Slide 14: A Two-Valued Boolean Algebra
(+) = OR, () = AND
OR AND
 | 0 | 1
0 | 0 | 1
1 | 1 | 1
x
y
 | 0 | 1
0 | 0 | 0
1 | 0 | 1
x
y
Can verify that all the postulates hold by “perfect induction.” [Checking that equality holds for all possible variable settings]

## Slide 15: Boolean Formulas and Functions
Example:
Can be specified via a truth table.
X | Y | Z | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 16: Normal Forms
Consider the function:
A literal is an occurrence of a complemented or uncomplemented variable in a formula.
A product term is either a literal or a product (conjunction) of literals.
Disjunctive normal form: A Boolean formula written as a single product term or as a sum (disjunction) of product terms.

## Slide 17: Normal Forms
Consider the function:
A sum term is either a literal or a sum (disjunction) of literals.
Conjunctive normal form: A Boolean formula written as a single sum term or as a product (conjunction) of sum terms.

## Slide 18: Canonical Formulas
How to obtain a Boolean formula given a truth table?
X | Y | Z | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 19: Minterm Canonical Formula
X | Y | Z | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 20: m-Notation
can be written as
X | Y | Z | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 21: Maxterm Canonical Formula
X | Y | Z | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 22: M-Notation
can be written as
X | Y | Z | f
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0